## Slide 19
y(n) = x(-n)
y(n, t) = T[x(n-t)] = x(-n-t)
y(n-t) = x(-(n-t)) = x(-n + t)

## Slide 24: Convolution

## Slide 25
Instantaneous multiplication between two signals

## Slide 26
Instantaneous multiplication between two signals

## Slide 27
Convolution
Convolution is a mathematical operation used to express the relation between input and output of an LTI system. It relates input, output and impulse response of an LTI system as
y(t)=x(t)∗h(t)
types of convolutions:
Continuous convolution
Discrete convolution

## Slide 45
EVEN or ODD Signals Problem

## Slide 47
Static or Dynamic System Problem

## Slide 52: Fourier Series

## Slide 58
Joseph Fourier: 1768-1830
A Fourier series is an expansion of a periodic function f(x) in terms of an infinite sum of sines and cosines. Fourier Series makes use of the orthogonality relationships of the sine and cosine functions.

## Slide 59: Fourier series expansion is used for periodic signals to expand them in terms of their harmonics which are sinusoidal and orthogonal to one another
Periodic signal : CT – CTFS
DT– DTFS
Non Periodic Signals: CTFT and DTFT
Laplace Transform: Design Purpose (Continuous Signals) (CT)
Z Transform Design Purpose (Continuous Signals) (DT)

## Slide 62: Basic Fourier Series Expansion
X(t) = 2 sin wt + sin 2wt + 7 sin3wt + …………………
even harmonic odd harmonic
Where w = 2*pi*f
Trigonometric Fourier series
Complex exponential FS
Polar or Harmonic FS

## Slide 63
Trigonometric Expansion
X(t) = dc average value of x(t) +
a0 = dc component
an = cosine components of the harmonics
bn = sine components of the harmonics
x(t) = 4 + 3 cos 2wt + 5 sin2wt + 3cos 3wt + 6sin3wt+……………………
a0 = 4
A2 = 3
b2 = 5

## Slide 66
If x(t) symmetric about t axis then a0 = 0
X(t) – Even signal bn = 0
x(-t) = x(t)
x(t) --- odd signal an = 0
x(-t) = -x(t)

## Slide 67
For square wave Ao = 0
Bn= 0
An != 0
For sawtooth wave :
Ao= 0
An= 0
Bn =! 0

## Slide 70
The Fourier Transform is a tool that breaks a waveform (a function or signal) into an alternate representation, characterized by the sine and cosine functions of varying frequencies. The Fourier Transform shows that any waveform can be re-written as the sum of sinusoidal.

## Slide 71
Fourier Series gives us a method of decomposing periodic functions into their sinusoidal components. The Fourier Series can also be viewed as a special introductory case of the Fourier Transform, so no Fourier Transform tutorial is complete without a study of Fourier Series.
A Fourier Series, with period T, is an infinite sum of sinusoidal functions (cosine and sine), each with a frequency that is an integer multiple of 1/T (the inverse of the fundamental period). The Fourier Series also includes a constant, and hence can be written as: